## Slide 1
8086 MICROPROCESSOR
Unit - III
16-bit Microprocessors (8086 )
Architecture
Pin diagram
Physical address
Segmentation
Memory organization
Bus cycle
Instruction set
Addressing modes
Assembly Language Programming of 8086
Comparison of 8086 & 8088

## Slide 2
Microprocessor - 8086 Overview
8086 Microprocessor is an enhanced version of 8085 Microprocessor that was designed by Intel in 1976.
The 8086 microprocessor is a16-bit, N-channel, HMOS microprocessor. Where the HMOS is used for "High-speed Metal Oxide Semiconductor".
Intel 8086 is built on a single semiconductor chip and packaged in a 40-pin IC package. The type of package is DIP (Dual Inline Package).
It is a 16-bit Microprocessor having 20 address lines and 16 data lines It can directly address up to 220 = 1 Mbyte of memory.
It consists of powerful instruction set, which provides operations like multiplication and division easily.

## Slide 3
It has an instruction queue, which is capable of storing six instruction bytes from the memory resulting in faster processing.
It was the first 16-bit processor having 16-bit ALU, 16-bit registers, internal data bus, and 16-bit external data bus resulting in faster processing.
It is available in 3 versions based on the frequency of operation −
8086 → 5MHz, 8086-2 → 8MHz, 8086-1 → 10 MHz
It uses two stages of pipelining, i.e. Fetch Stage and Execute Stage, which improves performance.
Fetch stage can prefetch upto 6 bytes of instructions and stores them in the queue.
Features of 8086
The most prominent features of a 8086 microprocessor are as follows :
8086 supports two modes of operation, i.e. Maximum mode and Minimum mode.
Maximum mode is suitable for system having multiple processors
Minimum mode is suitable for system having a single processor.

## Slide 4
Difference between 8085 and 8086 Microprocessor
8085 Microprocessor 8086 Microprocessor | 
It is an 8-bit microprocessor. | It is a 16-bit microprocessor.
It has a 16-bit address line. | It has a 20-bit address line.
It has a 8-bit data bus. | It has a 16-bit data bus.
The memory capacity is 64 KB. | The memory capacity is 1 MB.
The Clock speed of this microprocessor is 3 MHz. | The Clock speed of this microprocessor varies between 5, 8 and 10 MHz for different versions.
It has five flags. | It has nine flags.
8085 microprocessor does not support memory segmentation. | 8086 microprocessor supports memory segmentation.
It does not support pipelining. | It supports pipelining.
It is accumulator based processor. | It is general purpose register based processor.
It has no minimum or maximum mode. | It has minimum and maximum modes.
In 8085, only one processor is used. | In 8086, more than one processor is used. An additional external processor can also be employed.
It contains less number of transistors compare to 8086 microprocessor. It contains about 6500 transistor. | It contains more number of transistors compare to 8085 microprocessor. It contains about 29000 in size.
The cost of 8085 is low. | The cost of 8086 is high.

## Slide 5
Functional units of 8086
Bus Interface Unit (BIU)
The segment registers, instruction pointer and 6-byte instruction queue are associated with the bus interface unit (BIU).
The BIU:
Handles transfer of data and addresses,
Fetches instruction codes, stores fetched instruction codes in first-in-first-out register set called a queue,
Reads data from memory and I/O devices,
Writes data to memory and I/O devices.
It relocates addresses of operands since it gets un-relocated operand addresses from EU. The EU tells the BIU from where to fetch instructions or where to read data.
BIU takes care of all data and addresses transfers on the buses for the EU like sending addresses, fetching instructions from the memory, reading data from the ports and the memory as well as writing data to the ports and the memory. EU and BIU are connected with the Internal Bus.

## Slide 6
BIU has the following functional parts:
It has the following functional parts −
Instruction queue − BIU contains the instruction queue. BIU gets upto 6 bytes of next instructions and stores them in the instruction queue. When EU executes instructions and is ready for its next instruction, then it simply reads the instruction from this instruction queue resulting in increased execution speed.
Segment register − BIU has 4 segment buses, i.e. CS, DS, SS& ES. It holds the addresses of instructions and data in memory, which are used by the processor to access memory locations. It also contains 1 pointer register IP, which holds the address of the next instruction to executed by the EU.
  CS − It stands for Code Segment. It is used for addressing a memory location in the code segment of the memory, where the executable program is stored.
  DS − It stands for Data Segment. It consists of data used by the program andis accessed in the data segment by an offset address or the content of other register that holds the offset address.
  SS − It stands for Stack Segment. It handles memory to store data and addresses during execution.
  ES − It stands for Extra Segment. ES is additional data segment, which is used by the string to hold the extra destination data.
Instruction pointer − It is a 16-bit register used to hold the address of the next instruction to be executed.
Fetching the next instruction while the current instruction executes is called pipelining.

## Slide 7
Execution Unit (EU)
The EU receives opcode of an instruction from the queue, decodes it and then executes it. While Execution, unit decodes or executes an instruction, then the BIU fetches instruction codes from the memory and stores them in the queue.
The BIU and EU operate in parallel independently. This makes processing faster.
General purpose registers, stack pointer, base pointer and index registers, ALU, flag registers (FLAGS), instruction decoder and timing and control unit constitute execution unit (EU).
General Purpose Registers: There are four 16-bit general purpose registers: AX (Accumulator Register), BX (Base Register), CX (Counter) and DX. Each of these 16-bit registers are further subdivided into 8-bit registers as shown below:
16-bit registers | 8-bit high-order registers | 8-bit low-order registers
AX | AH | AL
BX | BH | BL
CX | CH | CL
DX | DH | DL

## Slide 8
Index Register: The following four registers are in the group of pointer and index registers:
  Stack Pointer (SP)
  Base Pointer (BP)
  Source Index (SI)
  Destination Index (DI)
ALU: It handles all arithmetic and logical operations. Such as addition, subtraction, multiplication, division, AND, OR, NOT operations.
Flag Register: It is a 16?bit register which exactly behaves like a flip-flop, means it changes states according to the result stored in the accumulator. It has 9 flags and they are divided into 2 groups i.e. conditional and control flags.

## Slide 9
Carry flag − This flag indicates an overflow condition for arithmetic operations.
Auxiliary flag − When an operation is performed at ALU, it results in a carry/barrow from lower nibble (i.e. D0 – D3) to upper nibble (i.e. D4 – D7), then this flag is set, i.e. carry given by D3 bit to D4 is AF flag. The processor uses this flag to perform binary to BCD conversion.
Parity flag − This flag is used to indicate the parity of the result, i.e. when the lower order 8-bits of the result contains even number of 1’s, then the Parity Flag is set. For odd number of 1’s, the Parity Flag is reset.
Zero flag − This flag is set to 1 when the result of arithmetic or logical operation is zero else it is set to 0.
Sign flag − This flag holds the sign of the result, i.e. when the result of the operation is negative, then the sign flag is set to 1 else set to 0.
Overflow flag − This flag represents the result when the system capacity is exceeded.
Conditional Flags: It represents the result of the last arithmetic or logical instruction executed. Following is the list of conditional flags :

## Slide 10
Control flags controls the operations of the execution unit. Following is the list of control flags −
Trap flag − It is used for single step control and allows the user to execute one instruction at a time for debugging. If it is set, then the program can be run in a single step mode.
Interrupt flag − It is an interrupt enable/disable flag, i.e. used to allow/prohibit the interruption of a program. It is set to 1 for interrupt enabled condition and set to 0 for interrupt disabled condition.
Direction flag − It is used in string operation. As the name suggests when it is set then string bytes are accessed from the higher memory address to the lower memory address and vice-a-versa.
Control Flags

## Slide 11
Block Diagram of Intel 8086 Microprocessor (8086 Architecture)

## Slide 13
Pin diagram of 8086 microprocessor is as given below:

## Slide 14
Memory Segmentation in 8086 Microprocessor
Segmentation is the process in which the main memory of the computer is logically divided into different segments and each segment has its own base address. It is basically used to enhance the speed of execution of the computer system, so that the processor is able to fetch and execute the data from the memory easily and fast.
Need for Segmentation The Bus Interface Unit (BIU) contains four 16 bit special purpose registers called as Segment Registers
Code segment register (CS): is used for addressing memory location in the code segment of the memory, where the executable program is stored.
Data segment register (DS): points to the data segment of the memory where the data is stored.
Extra Segment Register (ES): also refers to a segment in the memory which is another data segment in the memory.
Stack Segment Register (SS): is used for addressing stack segment of the memory. The stack segment is that segment of memory which is used to store stack data.

## Slide 15
The number of address lines in 8086 is 20, 8086 BIU will send 20bit address, so as to access one of the 1MB memory locations.
The four segment registers actually contain the upper 16 bits of the starting addresses of the four memory segments of 64 KB each with which the 8086 is working at that instant of time.
A segment is a logical unit of memory that may be up to 64 kilobytes long.
Each segment is made up of contiguous memory locations.
It is an independent, separately addressable unit. Starting address will always be changing. It will not be fixed.
Note that the 8086 does not work the whole 1MB memory at any given time.
However, it works only with four 64KB segments within the whole 1MB memory.

## Slide 16
Below is the one way of positioning four 64 kilobyte segments within the 1M byte memory space of an 8086.

## Slide 17
The main advantages of segmentation are as follows:
  It provides a powerful memory management mechanism.
  Data related or stack related operations can be performed in different segments.
  Code related operation can be done in separate code segments.
  It allows to processes to easily share data.
  It allows to extend the address ability of the processor, i.e. segmentation allows the use of 16 bit registers to give an addressing capability of 1 Megabytes. Without segmentation, it would require 20 bit registers.
  It is possible to enhance the memory size of code data or stack segments beyond 64 KB by allotting more than one segment for each area.
Advantages of the Segmentation

## Slide 18
physical address calculation in 8086 Microprocessor

## Slide 19
physical address calculation in 8086 Microprocessor
1.The value of Code Segment (CS) Register is 4042H and the value of different offsets is as follows: BX: 2025H , IP: 0580H , DI: 4247H Calculate the effective address of the memory location pointed by the CS register.
The offset of the CS Register is the IP register.
Therefore, the effective address of the memory location pointed by the CS register is calculated as follows:
Effective address= Base address of CS register X 10H + Address of IP
= 4042H X 10H + 0580H = (40420 + 0580)H = 41000H
2. Calculate the effective address for the following register: SS: 3860H, SP: 1735H, BP: 4826H
Both SP and BP are the offsets for Stack Register (SS). The address calculated when BP is taken as the offset gives the starting address of the stack. The address when SP is taken as the offset denotes the memory location where the top of the stack lies.
Therefore, the effective address for both these cases is:
(SS X 10H) + SP = 3640H X 10H + 1735H
= 36400H + 1735H = 38135H
(SS X 10H) + BP = 3640H X 10H + 4826H
= 36400H + 4826H = 41226H

## Slide 20
Q3) The value of the DS register is 3032H. And the BX register contains a 16 bit value which is equal to 3032H. 0008H is added to BX. ADD BX, 0008H The register AX contains some value which needs to be stored at a location as follows: MOV [BX], AX Calculate the address at which the value of the AX will be stored.
After executing the first instruction, the value of BX Register is as follows: BX = 3040H
The BX register is an offset of the Data Segment (DS) register.
So, the location at which the value of the AX register will be stored is calculated as follows:
(DS X 10H) + BX = 3032H X 10H +3040H = 30320H + 3040H = 33360H
SEGMENT REGISTERS | OFFSET REGISTERS | FUNCTION
CS | IP | ADDRESS OF INSTRUCTION
DS | BX, SI,DI | ADDRESS OF DATA
SS | SP, BP | ADDRESS OF THE STACK
ES | BX, SI, DI | ADDRESSOF DATA FOR STRING OPERATIONS

## Slide 21
Differences between 8086 and 8088 microprocessors
Though the architecture and instruction set of both 8086 and 8088 processors are same, still there are differences between them.
Following is the table listing the differences between the two microprocessors:
 | 8086 microprocessor | 8088 microprocessor
 | The data bus is of 16 bits. | The data bus is of 8 bits.
 | It has 3 available clock speeds (5 MHz, 8 MHz (8086-2) and 10 MHz (8086-1)). | It has 2 available clock speeds (5 MHz, 8 MHz)
 | It has memory control pin (M/IO) signal. | It has complemented memory control pin (IO/M) signal of 8086.
 | It has Bank High Enable (BHE) signal. | It has Status Signal (SSO).
 | It can read or write either 8-bit or 16-bit word at the same time. | It can read only 8-bit word at the same time.
 | It has 6 byte instruction queue. | It has 4 byte instruction queue as it can fetch only 1 byte at a time.

## Slide 22
Data Transfer Instructions
Arithmetic Instructions
Bit Manipulation Instructions
String Instructions
Program Execution Transfer Instructions (Branch & Loop Instructions)
Processor Control Instructions
Iteration Control Instructions
Interrupt Instructions
Microprocessor - 8086 Instruction Sets
The 8086 microprocessor supports 8 types of instructions :

## Slide 23
Data Transfer instruction
All the instructions which perform data movement come under this category. The source data may be a register, memory location, port etc. the destination may be a register, memory location or port. The following instructions come under this category:
Instruction | Description
MOV | Moves data from register to register, register to memory, memory to register, memory to accumulator, accumulator to memory, etc.
LDS | Loads a word from the specified memory locations into specified register. It also loads a word from the next two memory locations into DS register.
LES | Loads a word from the specified memory locations into the specified register. It also loads a word from next two memory locations into ES register.
LEA | Loads offset address into the specified register.
LAHF | Loads low order 8-bits of the flag register into AH register.
SAHF | Stores the content of AH register into low order bits of the flags register.
XLAT/XLATB | Reads a byte from the lookup table.
XCHG | Exchanges the contents of the 16-bit or 8-bit specified register with the contents of AX register, specified register or memory locations.
PUSH | Pushes (sends, writes or moves) the content of a specified register or memory location(s) onto the top of the stack.
POP | Pops (reads) two bytes from the top of the stack and keeps them in a specified register, or memory location(s).
POPF | Pops (reads) two bytes from the top of the stack and keeps them in the flag register.
IN | Transfers data from a port to the accumulator or AX, DX or AL register.
OUT | Transfers data from accumulator or AL or AX register to an I/O port identified by the second byte of the instruction.

## Slide 24
Instructions of this group perform addition, subtraction, multiplication, division, increment, decrement, comparison, ASCII and decimal adjustment etc.
Arithmetic Instructions
The following instructions come under this category:
ADD | Adds data to the accumulator i.e. AL or AX register or memory locations.
ADC | Adds specified operands and the carry status (i.e. carry of the previous stage).
SUB | Subtract immediate data from accumulator, memory or register.
SBB | Subtract immediate data with borrow from accumulator, memory or register.
MUL | Unsigned 8-bit or 16-bit multiplication.
IMUL | Signed 8-bit or 16-bit multiplication.
DIV | Unsigned 8-bit or 16-bit division.
IDIV | Signed 8-bit or 16-bit division.
INC | Increment Register or memory by 1.
DEC | Decrement register or memory by 1.
Instruction | Description

## Slide 25
Instruction | Description
DAA | Decimal Adjust after BCD Addition: When two BCD numbers are added, the DAA is used after ADD or ADC instruction to get correct answer in BCD.
DAS | Decimal Adjust after BCD Subtraction: When two BCD numbers are added, the DAS is used after SUB or SBB instruction to get correct answer in BCD.
AAA | ASCII Adjust for Addition: When ASCII codes of two decimal digits are added, the AAA is used after addition to get correct answer in unpacked BCD.
AAD | Adjust AX Register for Division: It converts two unpacked BCD digits in AX to the equivalent binary number. This adjustment is done before dividing two unpacked BCD digits in AX by an unpacked BCD byte.
AAM | Adjust result of BCD Multiplication: This instruction is used after the multiplication of two unpacked BCD.
AAS | ASCII Adjust for Subtraction: This instruction is used to get the correct result in unpacked BCD after the subtraction of the ASCII code of a number from ASCII code another number.
CBW | Convert signed Byte to signed Word.
CWD | Convert signed Word to signed Doubleword.
NEG | Obtains 2's complement (i.e. negative) of the content of an 8-bit or 16-bit specified register or memory location(s).
CMP | Compare Immediate data, register or memory with accumulator, register or memory location(s).

## Slide 26
Logical Instructions
Instruction of this group perform logical AND, OR, XOR, NOT and TEST operations.
The following instructions come under this category:
Instruction | Description
AND | Performs bit by bit logical AND operation of two operands and places the result in the specified destination.
OR | Performs bit by bit logical OR operation of two operands and places the result in the specified destination.
XOR | Performs bit by bit logical XOR operation of two operands and places the result in the specified destination.
NOT | Takes one's complement of the content of a specified register or memory location(s).
TEST | Perform logical AND operation of a specified operand with another specified operand.

## Slide 27
Rotate Instructions
The following instructions come under this category:
Instruction | Description
RCL | Rotate all bits of the operand left by specified number of bits through carry flag.
RCR | Rotate all bits of the operand right by specified number of bits through carry flag.
ROL | Rotate all bits of the operand left by specified number of bits.
ROR | Rotate all bits of the operand right by specified number of bits.
Shift Instructions
The following instructions come under this category:
Instruction | Description
SAL or SHL | Shifts each bit of operand left by specified number of bits and put zero in LSB position.
SAR | Shift each bit of any operand right by specified number of bits. Copy old MSB into new MSB.
SHR | Shift each bit of operand right by specified number of bits and put zero in MSB position.

## Slide 28
Branch Instructions
It is also called program execution transfer instruction. Instructions of this group transfer program execution from the normal sequence of instructions to the specified destination or target.
The following instructions come under this category:
Instruction | Description
JA or JNBE | Jump if above, not below, or equal i.e. when CF and ZF = 0
JAE/JNB/JNC | Jump if above, not below, equal or no carry i.e. when CF = 0
JB/JNAE/JC | Jump if below, not above, equal or carry i.e. when CF = 0
JBE/JNA | Jump if below, not above, or equal i.e. when CF and ZF = 1
JCXZ | Jump if CX register = 0
JE/JZ | Jump if zero or equal i.e. when ZF = 1
JG/JNLE | Jump if greater, not less or equal i.e. when ZF = 0 and CF = OF
JGE/JNL | Jump if greater, not less or equal i.e. when SF = OF
JL/JNGE | Jump if less, not greater than or equal i.e. when SF ≠ OF
JLE/JNG | Jump if less, equal or not greater i.e. when ZF = 1 and SF ≠ OF
JMP | Causes the program execution to jump unconditionally to the memory address or label given in the instruction.
CALL | Calls a procedure whose address is given in the instruction and saves their return address to the stack.
RET | Returns program execution from a procedure (subroutine) to the next instruction or main program.
IRET | Returns program execution from an interrupt service procedure (subroutine) to the main program.
INT | Used to generate software interrupt at the desired point in a program.
INTO | Software interrupts to indicate overflow after arithmetic operation.
LOOP | Jump to defined label until CX = 0.
LOOPZ/LOOPE | Decrement CX register and jump if CX ≠ 0 and ZF = 1.
LOOPNZ/LOOPNE | Decrement CX register and jump if CX ≠ 0 and ZF = 0.

## Slide 29
Flag Manipulation and Processor Control Instructions
Instructions of this instruction set are related to flag manipulation and machine control.
The following instructions come under this category:
Instruction | Description
CLC | Clear Carry Flag: This instruction resets the carry flag CF to 0.
CLD | Clear Direction Flag: This instruction resets the direction flag DF to 0.
CLI | Clear Interrupt Flag: This instruction resets the interrupt flag IF to 0.
CMC | This instruction take complement of carry flag CF.
STC | Set carry flag CF to 1.
STD | Set direction flag to 1.
STI | Set interrupt flag IF to 1.
HLT | Halt processing. It stops program execution.
NOP | Performs no operation.
ESC | Escape: makes bus free for external master like a coprocessor or peripheral device.
WAIT | When WAIT instruction is executed, the processor enters an idle state in which the processor does no processing.
LOCK | It is a prefix instruction. It makes the LOCK pin low till the execution of the next instruction.

## Slide 30
String Instructions
String is series of bytes or series of words stored in sequential memory locations. The 8086 provides some instructions which handle string operations such as string movement, comparison, scan, load and store.
The following instructions come under this category:
Instruction | Description
MOVS/MOVSB/MOVSW | Moves 8-bit or 16-bit data from the memory location(s) addressed by SI register to the memory location addressed by DI register.
CMPS/CMPSB/CMPSW | Compares the content of memory location addressed by DI register with the content of memory location addressed by SI register.
SCAS/SCASB/SCASW | Compares the content of accumulator with the content of memory location addressed by DI register in the extra segment ES.
LODS/LODSB/LODSW | Loads 8-bit or 16-bit data from memory location addressed by SI register into AL or AX register.
STOS/STOSB/STOSW | Stores 8-bit or 16-bit data from AL or AX register in the memory location addressed by DI register.
REP | Repeats the given instruction until CX ≠ 0
REPE/ REPZ | Repeats the given instruction till CX ≠ 0 and ZF = 1
REPNE/REPNZ | Repeats the given instruction till CX ≠ 0 and ZF = 0

## Slide 31
Addressing modes of 8086
The way for which an operand is specified for an instruction in the accumulator, in a general purpose register or in memory location, is called addressing mode.
The 8086 microprocessors have 8 addressing modes. Two addressing modes have been provided for instructions which operate on register or immediate data.
These two addressing modes are:
Register Addressing: In register addressing, the operand is placed in one of the 16-bit or 8-bit general purpose registers.
Example
MOV AX, CX
ADD AL, BL
ADD CX, DX
Immediate Addressing: In immediate addressing, the operand is specified in the instruction itself.
Example
MOV AL, 35H
MOV BX, 0301H
MOV [0401], 3598H
ADD AX, 4836H

## Slide 32
The remaining 6 addressing modes specify the location of an operand which is placed in a memory.
These 6 addressing modes are:
The remaining 6 addressing modes specify the location of an operand which is placed in a memory.
These 6 addressing modes are:
Direct Addressing: In direct addressing mode, the operands offset is given in the instruction as an 8-bit or 16-bit displacement element.
Example
ADD AL, [0301]
The instruction adds the content of the offset address 0301 to AL. the operand is placed at the given offset (0301) within the data segment DS.
Register Indirect Addressing: The operand's offset is placed in any one of the registers BX, BP, SI or DI as specified in the instruction.
Example
MOV AX, [BX]
It moves the contents of memory locations addressed by the register BX to the register AX.

## Slide 33
Based Addressing: The operand's offset is the sum of an 8-bit or 16-bit displacement and the contents of the base register BX or BP. BX is used as base register for data segment, and the BP is used as a base register for stack segment.
Effective address (Offset) = [BX + 8-bit or 16-bit displacement].
Example
MOV AL, [BX+05]; an example of 8-bit displacement.
MOV AL, [BX + 1346H]; example of 16-bit displacement.
Indexed Addressing: The offset of an operand is the sum of the content of an index register SI or DI and an 8-bit or 16-bit displacement.
Offset (Effective Address) = [SI or DI + 8-bit or 16-bit displacement]
Example : MOV AX, [SI + 05]; 8-bit displacement.
MOV AX, [SI + 1528H]; 16-bit displacement.
Based Indexed Addressing: The offset of operand is the sum of the content of a base register BX or BP and an index register SI or DI.
Effective Address (Offset) = [BX or BP] + [SI or DI]
Here, BX is used for a base register for data segment, and BP is used as a base register for stack segment.
Example: ADD AX, [BX + SI]
MOV CX, [BX + SI]

## Slide 34
Based Indexed with Displacement: In this mode of addressing, the operand's offset is given by:
Effective Address (Offset) = [BX or BP] + [SI or DI] + 8-bit or 16-bit displacement
Example
MOV AX, [BX + SI + 05]; 8-bit displacement
MOV AX, [BX + SI + 1235H]; 16-bit displacement

## Slide 35
ASSEMBLER DIRECTIVES :
Assembler directives are the directions to the assembler which indicate how an
operand or section of the program is to be processed. These are also called
pseudo operations which are not executable by the microprocessor.
The various directives are explained below.
ASSUME : The ASSUME directive is used to inform the assembler the name of the logical segment it should use for a specified segment.
Ex: ASSUME DS: DATA tells the assembler that for any program instruction which refers to the data segment ,it should use the logical segment called DATA.
DB -Define byte. It is used to declare a byte variable or set aside one or more storage locations of type byte in memory.
For example, CURRENT_VALUE DB 36H tells the assembler to reserve 1 byte of memory for a variable named CURRENT_ VALUE and to put the value 36 H in that memory location when the program is loaded into RAM .
DW -Define word. It tells the assembler to define a variable of type word or to reserve storage locations of type word in memory.

## Slide 36
DD(define double word) :This directive is used to declare a variable of type double word or restore memory locations which can be accessed as type double word.
DQ (define quadword) :This directive is used to tell the assembler to declare a variable 4 words in length or to reserve 4 words of storage in memory .
DT (define ten bytes):It is used to inform the assembler to define a variable which is 10 bytes in length or to reserve 10 bytes of storage in memory.
EQU –Equate It is used to give a name to some value or symbol. Every time the assembler finds the given name in the program, it will replace the name with the value or symbol we have equated with that name
ORG-Originate : The ORG statement changes the starting offset address of the data.
It allows to set the location counter to a desired value at any point in the program.For example the statement ORG 3000H tells the assembler to set the location counter to 3000H.

## Slide 37
Memory data lines must be connected to either the
upper half AD15-AD0 or lower half AD7-AD0 of the 8086 data lines.

## Slide 38
PROC- Procedure: It is used to identify the start of a procedure or subroutine.
ENDP-End procedure: It indicates the end of the procedure (subroutine) to the assembler.
CODE SEGMENT : Start of logical segment containing
code
code ends: End of the segment named CODE
ENDS-End Segment: This directive is used with the name of the segment to indicate the end of that logical segment.
END- End program .This directive indicates the assembler that
this is the end of the program module.The assembler ignores any statements
after an END directive.

## Slide 39
To communicate with the outside world microcomputers use peripherals (I/O devices). Commonly used peripherals are: A/D converter, D/A converter, CRT, printers, Hard disks, floppy disks, magnetic tapes etc.
Peripheral Devices
A programmable peripheral interface is a multiport device. The ports may be programmed in a variety of ways as required by the programmer. The device is very useful for interfacing peripheral devices.
Peripherals are connected to the microcomputer through electronic circuits known as interfacing circuits.
Programmable Peripheral interface (PPI)
The Intel 8255 is a programmable peripheral interface (PPI). It has two versions, namely the Intel 8255A and Intel 8255A-5. General descriptions for both are same. There are some differences in their electrical characteristics. Hereafter, they will be referred to as 8255. Its main functions are to interface peripheral devices to the microcomputer.8M
It has three 8-bit ports, namely Port A, Port B and Port C. The port C has been further divided into two 4-bit ports, port C upper and Port C lower. Thus a total of 4-ports are available, two 8-bit ports and two 4-bit ports. Each port can be programmed either as an input port or an output port.
Intel 8255

## Slide 40
Memory & I/O Interfacing
Data Transfer Schemes
Interfacing Devices: PPI (Intel8255), PCI (Intel8251), 8257(DMA),PIC (Intel8259), Intel8253
UNIT IV
Following major topics will be covered in this unit
PPI: PROGRAMMABLE PERIPHERAL INTERFACE Intel 8255

## Slide 41
PPI 8255 is a general purpose programmable I/O device designed to interface the CPU with its outside world such as ADC, DAC, keyboard etc. We can program it according to the given condition. It can be used with almost any microprocessor.
It consists of three 8-bit bidirectional I/O ports i.e. PORT A, PORT B and PORT C. We can assign different ports as input or output functions.
PPI: PROGRAMMABLE PERIPHERAL INTERFACE Intel 8255

## Slide 44
THE PIN DETAILS OF 8255
PA0 – PA7 – Pins of port A
PB0 – PB7 – Pins of port B
PC0 – PC7 – Pins of port C
D0 – D7 – Data pins for the transfer of data
RESET – Reset input
RD’ – Read input
WR’ – Write input
CS’ – Chip select
A1 and A0 – Address pins

## Slide 47
Mode 0 –In this mode all the three ports (port A, B, C) can work as simple input function or simple output function. In this mode there is no interrupt handling capacity.
Mode 2 – Bi-directional data bus mode. In this mode only port A works, and port B can work either in mode 0 or mode 1. 6 bits port C are used as handshake signals. It also has interrupt handling capacity.
Mode 1 – Handshake I/O mode or strobed I/O mode. In this mode either port A or port B can work as simple input port or simple output port, and port C bits are used for handshake signals before actual data transmission. It has interrupt handling capacity and input and output are latched.Example: A CPU wants to transfer data to a printer. In this case since speed of processor is very fast as compared to relatively slow printer, so before actual data transfer it will send handshake signals to the printer for synchronization of the speed of the CPU and the peripherals.
I/O MODE

## Slide 49
This mode affects only one bit of port C at a time because, as user set the bit, it remains set until and unless user changes it. User needs to load the bit pattern in control register to change the bit
This mode is used to set or reset the bits of port C only, and selected when the most significant bit (D7) in the control register is 0. Control Register is as follows:
Bit set reset (BSR) mode
PORT C BITS | D3 | D2 | D1
PCO | 0 | 0 | 0
PC1 | 0 | 0 | 1
PC2 | 0 | 1 | 0
PC3 | 0 | 1 | 1
PC4 | 1 | 0 | 0
PC5 | 1 | 0 | 1
PC6 | 1 | 1 | 0
PC7 | 1 | 1 | 1

## Slide 50
It consists of 40 pins and operates in +5V regulated power supply. Port C is further divided into two 4-bit ports i.e. port C lower and port C upper and port C can work in either BSR (bit set rest) mode or in mode 0 of input-output mode of 8255. Port B can work in either mode 0 or in mode 1 of input-output mode. Port A can work either in mode 0, mode 1 or mode 2 of input-output mode.
It has two control groups, control group A and control group B. Control group A consist of port A and port C upper. Control group B consists of port C lower and port B.
Depending upon the value if CS’, A1 and A0 we can select different ports in different modes as input-output function or BSR. This is done by writing a suitable word in control register (control word D0-D7).
CS’ | A1 | A0 | Selection | Address
0 | 0 | 0 | PORT A | 80 H
0 | 0 | 1 | PORT B | 81 H
0 | 1 | 0 | PORT C | 82 H
0 | 1 | 1 | Control Register | 83 H
1 | X | X | No Seletion | X

## Slide 51
Bit set reset (BSR) mode If MSB of control word (D7) is 0, PPI works in BSR mode. In this mode only port C bits are used for set or reset.
Operating modes

## Slide 52
Introduction to Serial communication:
Most of the microprocessors are designed for parallel communication.
> In parallel communication number of lines required to transfer data depend on the number of bits to be transmitted.
> For transmitting data over long distance, using parallel communication is impractical due to the increase in cost of cabling.
> In such cases serial communication is used.
> In serial communication one bit is transferred at a time over a single line.
> Serial communication can be classified on the basis how transmission occurs.
1. Simplex: In simplex, the hardware such that data transfer takes place in only one direction.
Ex: Computer to Printer communication
2. Half Duplex: The half duplex transmission allows the data transfer in both direction but not simultaneously.
Ex: Walkie talkie
3. Full Duplex: It allows the data transfer in both direction simultaneously.
Ex: Telephone lines

## Slide 53
1. Programmed data transfer scheme
2. DMA (Direct Memory Access) data transfer scheme
1. Programmed data transfer scheme
DATA TRANSFER SCHEMES
To solve the problem of speed mismatch between microprocessor and I/O device
A number of data transfer techniques have been developed
The data transfer schemes are classified into the following two categories:
Programmed data transfer scheme s are controlled by the CPU
Data are transferred from an I/O device to CPU (or to the memory through CPU) or vice versa
Programmed data transfer scheme are employed when small amount of data are to be transferred
Synchronous data transfer scheme
Asynchronous data transfer scheme
Interrupt driven data transfer scheme
The programmed data transfer schemes are classified into the following three categories:

## Slide 54
Data transfer schemes:
1. Asynchronous:
> Asynchronous formats are character oriented.
> In this type the bits or character or data word are sent at constant rate, but characters can come
at any rate (asynchronously) as long as they do not overlap.
> When no characters are being sent a line stays high at logic1 called mark, logic0 is called space.
> The beginning of a character is indicated by start bit which is always low.
> This is used to synchronize the transmitter and receiver.
> After the start bit the data bits are sent with least significant bit first followed by one or more stop bits (active high).
> The stop bits indicate the end of character.
> The combination of start bIt character and stop bits is known as frame.
The start and stop bits carry no information, but are required because of asynchronous nature of data.

## Slide 55
Synchronous:
The start and stop bits in each frame of asynchronous format represents wasted overhead bytes that reduce overall character rate.
These start and stop bits can be eliminated by synchronizing receiver and transmitter.
They can be synchronized by having a common clock signal.
Such a communication is called synchronous serial communication.
In this transmission synchronous bits are inserted instead of start and stop bits

## Slide 57
 | S.No | Asynchronous | Synchronous
 | 1. | Transmitters and receivers are notsynchronizedby clock. | Transmittersandreceiversaresynchronizedbyclock.
 | 2. | Bits of data are transmitted at constantrate. | Databitsaretransmittedwithsynchronizationofclock.
 | 3. | Character may arrive at any rate atreceiver. | Characterisreceivedatconstantrate.
 | 4. | Datatransferischaracteroriented. | Datatransfertakesplaceinblocks
 | 5. | Start and stop bits are required toestablish communication of eachcharacter. | Start and stop bits are not required to establish communication ofeach character. Synchronization bits are required to transfer thedatablock.
 | 6. | Used in low-speed transmission at aboutspeedless than20Kbits/sec. | Usedinhighspeedtransmissions.
RATE OF TRANSMISSION (BAUD RATE)
The data rate can be expressed as bit/sec or character/sec.
The term bit/sec is also called baudrate.

## Slide 58
In DMA data transfer scheme CPU does not participate
Data are directly transferred from an I/O device to the memory or vice versa
The data transfer is controlled by the I/O device or a DMA controller
The scheme is employed when large amount of data are to be transferred
An I/O device which wants to send data using DMA technique, sends the HOLD signal to the CPU
On receiving a HOLD signal the CPU gives up the control of buses on completion of machine cycle
DMA data transfer scheme
The CPU sends a hold acknowledge signal to the I/O device to indicate
It has received the HOLD request and it has released the buses
DMA transfer scheme is a faster scheme as compared to programmed data transfer scheme
It is used to transfer data from mass storage devices such as hard disk, optical disk etc.
DMA data transfer are of the following two types:
Burst mode of DMA transfer
Cycle stealing technique of DMA data transfer

## Slide 59
In which the I/O device withdraws the DMA request only after all the data bytes have been transferred
Called burst mode of data transfer
By this technique a block of data is transferred
This technique is employed by magnetic disk drives
In case of magnetic disks data transfer can not be stopped or slowed down without loss of data
Hence, block transfer is must
Burst mode of DMA transfer
In this technique a long block of data is transferred by a sequence of DMA cycles
In this method after transferring one byte or several bytes the I/O device withdraws DMA request
This method reduces interference in CPU’s activities
The interference can be eliminated completely by designing an interference circuitry
Which can steal bus cycle for DMA data transfer only when the CPU is not using the system bus
Examples of DMA controller chips are: Intel 8237A, 8257 etc.
Cycle stealing technique of DMA data transfer

## Slide 60
To transmit byte data it is necessary to convert byte into eight serial bits.
This can be done by using the parallel to serial converter.
Similarly at the reception these serial bits must be converted into parallel 8-bit data.
The serial to parallel converter is used to convert serial data bits into parallel data.
The devices are designed for this purpose are called universal synchronous asynchronous receiver-transmitter.
These devices are software programmable for number of data bits, parity and number of stop bits.
8251- Universal Synchronous Asynchronous Receiver-Transmitter (USART) Architecture:
Memory & I/O Interfacing
Data Transfer Schemes
Interfacing Devices: PPI (Intel8255), USART (Intel8251), 8257(DMA),PIC (Intel8259), Intel8253
UNIT IV
Following major topics will be covered in this unit
To implement serial communication in microprocessor system we need basically two devices:
1. Parallel to Serial Converter
2. Serial to Parallel Converter

## Slide 62
Transmit Buffer:
> The transmit buffer accepts parallel data from CPU, adds the appropriate framing information, serializes it and transmits it on the TxD pin on the failing edge of TxC'
Transmit Control:
> It manages all activities associated with the transmission of serial data.
> It accepts and issues signals both externally and internally to accomplish this function.
Data Bus Buffer:
> This bidirectional 8-bit buffer is used to interface 8251 to the system data bus.
> Along with the data, control word, command words and status information are also transferred through the Data Bus Buffer.
Read/Write Control Logic:
> This functional block accepts inputs from the system control bus and generates control signals for over all operation.
> It contains the control word register and command word register that stores the various control formats for the device functional definitions.
Ø Receiver Buffer:
The receiver buffer accepts serial data on the RxD line, coverts this serial data to parallel formats, checks for bits or characters that are unique to the communication technique and sends an “assembled” character to CPU.
Receiver Control:
It manages all activities associated with the receiving of serial data.
Along with data reception, it does false start bit detection, parity error detection, framing error detection, sync detection and break detection.

## Slide 63
Modem Control:
Ø The 8251 has set of control inputs and outputs that can be used to simplify the interface to almost any modem.
Ø Data Bus (D0-D7): This pin allows transfer of data bytes between CPU and the 8251A.
Ø Read (RD’) : A low on this input allows CPU to read data or status byte from 8251A.
Ø Write (WR’) : A low on this input allows CPU to write data or command word to 8251A.
Ø Clock (CLK): The CLK input is used to generate internal device timing.
Ø RESET: A high on this input force 8251A into an “IDLE” mode.
Ø Control/Data (C/ D’): This input in conjunction with the WR’ and the RD’ inputs informs the 8251A that the word on the DATA BUS is either a data character, control word or status information.
Ø Chip Select (CS’): A low on this input allows communication between CPU and 8251A.
The 8251 functional configuration is programed by software. Operation between the 8251 and a CPU is executed by program control. Table: shows the operation between a CPU and the device.

## Slide 64
1) Mode Instruction
Mode instruction is used for setting the function of the 8251. Mode instruction will be in "wait for write" at either internal reset or external reset. That is, the writing of a control word after resetting will be recognized as a "mode instruction."
Items set by mode instruction are as follows:
Synchronous/asynchronous mode
Stop bit length (asynchronous mode)
Character length
Parity bit
Baud rate factor (asynchronous mode)
Internal/external synchronization (synchronous mode)
Number of synchronous characters (Synchronous mode)
The bit configuration of mode instruction is shown in Figures 2 and 3. In the case of synchronous mode, it is necessary to write one-or two byte sync characters. If sync characters were written, a function will be set because the writing of sync characters constitutes part of mode instruction.
Control Words
There are two types of control word. 1.Mode instruction (setting of function) 2.Command (setting of operation)

## Slide 68
DSR (Input terminal)
This is an input port for MODEM interface. The input status of the terminal can be recognized by the CPU reading status words.
DTR (Output terminal)
This is an output port for MODEM interface. It is possible to set the status of DTR by a command.
CTS (Input terminal)
This is an input terminal for MODEM interface which is used for controlling a transmit circuit. The terminal controls data transmission if the device is set in "TX Enable" status by a command. Data is transmitable if the terminal is at low level.
RTS (Output terminal)
This is an output port for MODEM interface. It is possible to set the status RTS by a command.

## Slide 69
A programmable counter/interval timer is used in real time application
For timing and counting function such as BCD/ binary counting generation of accurate time delay
Generation of square wave of desired frequency, rate generation,
Hardware/software triggered strobe signals, One shot signal of desired width etc..
Popular programmable interval timer chips are Intel 8253 and Intel 8254
Both are pin to pin compatible, operates in six modes
Programmable Counter/Interval Timer

## Slide 70
  Six programmable timer modes allow the 82C54 / 8253 to be used as
  an event counter, elapsed time indicator, programmable one-shot,
  and in many other applications.
Programmable Interval Timer 8253
  The Intel 8253 is a programmable counter / timer chip designed for use as an Intel microcomputer peripheral. It uses nMOS technology with a single +5V supply and is packaged in a 24-pin plastic DIP.
  It is organized as 3 independent 16-bit counters, each with a counter rate up to 2 MHz. All modes of operation are software programmable.

## Slide 71
Programmable Interval Timer 8253
The block labeled data bus buffer contains the logic to buffer the data bus to / from the microprocessor, and to the internal registers.
The block labeled read / write logic controls the reading and the writing of the counter registers.
the control word register, contains the programmed information that is sent to the device from the microprocessor. In effect this register defines how the 8253 logically works.
The timer has three independent, programmable counters and they are all identical. Each counter in the block diagram has 3 logical lines connected to it.
Fig: Block diagram of an 8253 programmable interval timer
Two of these lines, clock and gate, are inputs. The third, labeled OUT is an output.
The function of these lines changes and depends on how the device is initialized or programmed.

## Slide 72
The following picture shows the pin configuration of the 8253 and a general definition of the lines follows:
8253: PIN configuration
  Clock This is the clock input for the counter. The counter is 16 bits. The maximum clock frequency is 1 / 380 nanoseconds or 2.6 megahertz. The minimum clock frequency is DC or static operation.
  Out This single output line is the signal that is the final programmed output of the device. Actual operation of the outline depends on how the device has been programmed.
  Gate This input can act as a gate for the clock input line, or it can act as a start pulse, depending on the programmed mode of the counter.

## Slide 73
C͞ S: Chip Select
W͞ R: Write, when it is low the CPU outputs data in the form mode information or loading of counters
R͞ D: Read, when it is low the CPU reads data
D0 – D7: Bidirectional data bus
A0, A1: These pins are connected to the address bus, these are used select on of the three counters
These are also used the address the control word registers for mode selection
CLK0, CLK1 and CLK2 are clock for Counter 0, Counter 1, and Counter 2 respectively
GATE0, GATE1 and GATE2 are gate terminals of Counter 0, Counter 1 and Counter 2
OUT0, OUT1 and OUT2 are output terminals of Counter 0, Counter 1 and Counter 2
VCC: Operating voltage
GND: Ground
The 8253 contains a data bus buffer, read/write logic and Control Word registers
THE PIN DETAILS OF INTEL 8253

## Slide 74
list of the internal 8253 registers that will program the internal counters of the 8253:
INTERNAL 8253 REGISTER

## Slide 75
This internal register is used to write information to, prior to using the device. This register is addressed when A0 and A1 inputs are logical 1's. The data in the register controls the operation mode and the selection of either binary or BCD ( binary coded decimal ) counting format. The register can only be written to. You can't read information from the register.
Control Word Register
Control Word Register
All of the operating modes for the counters are selected by writing bytes to the control register. This is the control word format.

## Slide 76
Bits D7 and D6 are labeled SC1 and SC0. These bits select the counter to be programmed, it is necessary to define, using the control bits D7 and D6, which counter is being set up.
Once a counter is set up, it will remain that way until it is changed by another control word
.
control word format

## Slide 77
Mode 0: Interrupt on terminal count
Mode 1: Programmable one-shot
Mode 2: Rate generator
Mode 3: Square wave generator
Mode 4: Software triggered mode
Mode 5: Hardware triggered mode
OPERATING MODES OF INTEL 8253
The Intel 8253 operates in the following six modes:

## Slide 78
Programmable Interrupt Controller (PIC)
• The programmable interrupt controller is used when several I/O devices transfer data using
interrupt
• They are to be connected to the same interrupt line of the microprocessor
• When the number of I/O devices is less than the number of interrupt lines of the
microprocessor
• Such controllers are not required
Intel 8259
• The Intel 8259 is a single chip programmable interrupt controller
• It is compatible with 8086, 8088 and 8085 microprocessor
• It is a 28-pin I.C. package and uses N-MOS technology
• It requires a single +5V supply for its operation
If we are working with an 8086, we have a problem here because the 8086 has only two interrupt inputs, NMI and INTR.
If we save NMI for a power failure interrupt, this leaves only one interrupt for all the other applications. For applications where we have interrupts from multiple source, we use an external device called a priority interrupt controller (PIC) to the interrupt signals into a single interrupt input on the processor.

## Slide 79
Schematic Diagram of Intel 8259

## Slide 81
Interfacing of Intel 8259 and I/O Devices
Internal Registers of 8259
Interrupt Request Register (IRR):
• It stores the interrupt request
• It keeps information about the interrupts inputs which have requested for interrupt service
• When an interrupt request is received, the corresponding bit in IRR is set
In-Service Register (ISR):
• Which interrupt is currently being serviced, this information is stored in the ISR
• The bit corresponding to the interrupt of the highest priority is selected
Interrupt Mask Register (IMR):
• It contains a specific bit for each interrupt line
• It is used to mask (disable) or enable (unmask) individual interrupt input
• An interrupt input can be masked by setting the corresponding bit to 1 in IMR
• An interrupt which is masked by software is not recognized and serviced
• Even if the corresponding bit is set in the IRR
• The 82C59 is the CHMOS version of NMOS 8259
• It consumes less power

## Slide 82
Priority Resolver : This unit determines the priorities of the interrupt requests appearing simultaneously. The highest priority is selected and stored into the corresponding bit of ISR during INTA pulse. The IR0 has the highest priority while the IR7 has the lowest one, normally in fixed priority mode. The priorities however may be altered by programming the 8259A in rotating priority mode.
Interrupt Mask Register (IMR) : This register stores the bits required to mask the interrupt inputs. IMR operates on IRR at the direction of the Priority Resolver.
Interrupt Control Logic: This block manages the interrupt and interrupt acknowledge signals to be sent to the CPU for serving one of the eight interrupt requests. This also accepts the interrupt acknowledge (INTA) signal from CPU that causes the 8259A to release vector address on to the data bus.

## Slide 83
Data Bus Buffer : This tristate bidirectional buffer interfaces internal 8259A bus to the microprocessor system data bus. Control words, status and vector information pass through data buffer during read or write operations.
Read/Write Control Logic: This circuit accepts and decodes commands from the CPU. This block also allows the status of the 8259A to be transferred on to the data bus.
Cascade Buffer/Comparator: This block stores and compares the ID’s all the 8259A used in system. The three I/O pins CASO-2 are outputs when the 8259A is used as a master. The same pins act as inputs when the 8259A is in slave mode. The 8259A in master mode sends the ID of the interrupting slave device on these lines. The slave thus selected, will send its preprogrammed vector address on the data bus during the next INTA pulse.
CS: This is an active-low chip select signal for enabling RD and WR operations of 8259A. INTA function is independent of CS.
WR : This pin is an active-low write enable input to 8259A. This enables it to accept command words from CPU.
RD : This is an active-low read enable input to 8259A. A low on this line enables 8259A to release status onto the data bus of CPU.
D0-D7 : These pins from a bidirectional data bus that carries 8-bit data either to control word or from status word registers. This also carries interrupt vector information.
CAS0 – CAS2 Cascade Lines : A signal 8259A provides eight vectored interrupts. If more interrupts are required, the 8259A is used in cascade mode. In cascade mode, a master 8259A along with eight slaves 8259A can provide upto 64 vectored interrupt lines. These three lines act as select lines for addressing the slave 8259A.

## Slide 85
The Details of Pins of Intel 8259
• C͞S: Chip Select
• W͞R: Write, A low on this pin enables Intel 8259 to accept command from CPU
• R͞D: Read, A low on this pin enables Intel 8259 to send various status signals on data bus for
CPU
• D0 – D7: Bidirectional data bus, control, status and interrupt information are transferred via
this bus
• CAS0 – CAS1: Cascade lines
• S͞P/ E͞N: Slave program/ Enable buffer, it is related to cascade control
• INT: Interrupt, it is used to interrupt CPU
• INTA: Interrupt acknowledge
• IR0 – IR7: Interrupt requests, I/O devices send interrupt request through these lines
• A0: Address line, it acts in conjunction with R͞D, W͞R and C͞S
• 8 I/O devices can be connected to Intel 8259 through IR0 – IR7 lines
• The interrupt controller functions as overall manager in an interrupt driven system• If more than one I/O devices send interrupt request at the same time, the interrupt controllers
set the priority

## Slide 86
8527 DMA CONTROLLER
Initially, when any device has to send data between the device and the memory, the device has to send DMA request (DRQ) to DMA controller.
The DMA controller sends Hold request (HRQ) to the CPU and waits for the CPU to assert the HLDA.
Then the microprocessor tri-states all the data bus, address bus, and control bus. The CPU leaves the control over bus and acknowledges the HOLD request through HLDA signal.
Now the CPU is in HOLD state and the DMA controller has to manage the operations over buses between the CPU, memory, and I/O devices.
DMA stands for Direct Memory Access. It is designed by Intel to transfer data at the fastest rate. It allows the device to transfer the data directly to/from memory without any interference of the CPU.
Using a DMA controller, the device requests the CPU to hold its data, address and control bus, so the device is free to transfer data directly to/from the memory. The DMA data transfer is initiated only after receiving HLDA signal from the CPU.
Following is the sequence of operations performed by a DMA :

## Slide 87
FEATURES OF 8257
It has four channels which can be used over four I/O devices.
Each channel has 16-bit address and 14-bit counter.
Each channel can transfer data up to 64kb.
Each channel can be programmed independently.
Each channel can perform read transfer, write transfer and verify transfer operations.
It generates MARK signal to the peripheral device that 128 bytes have been transferred.
It requires a single phase clock.
Its frequency ranges from 250Hz to 3MHz.
It operates in 2 modes, i.e., Master mode and Slave mode.

## Slide 88
The 8527 controller has four independent channels each of which contains an address register and a counter. The counter decrements as each byte transfer occur, and forces termination of the DMA operation after the last transfer.
The controller increments the address registers after each operation, so that successive data transfers are made at contiguous ascending addresses.
The arbiter resolves conflicts among the channels for access to memory.
Two methods have been used in this chip to make the chip useful in a variety of different applications.
In one mode the channels have a fixed priority and conflicts are resolved according to the priority, for example, Channel 0 has highest priority and Channel 3 lowest.
The second mode is a rotating priority scheme in which priority rankings are the four cycle shifts of 0-1-2-3, when a channel is granted access to the bus the priority ranking shifts cyclically to place the channel in the lowest priority position for the next arbitration cycle.

## Slide 89
8257 ARCHITECTURE

## Slide 90
8257 Pin Description
The following image shows the pin diagram of a 8257 DMA controller

## Slide 91
DRQ0−DRQ3
These are the four individual channel DMA request inputs, which are used by the peripheral devices for using DMA services. When the fixed priority mode is selected, then DRQ0 has the highest priority and DRQ3 has the lowest priority among them.
DACKo − DACK3
These are the active-low DMA acknowledge lines, which updates the requesting peripheral about the status of their request by the CPU. These lines can also act as strobe lines for the requesting devices.
Do − D7
These are bidirectional, data lines which are used to interface the system bus with the internal data bus of DMA controller. In the Slave mode, it carries command words to 8257 and status word from 8257. In the master mode, these lines are used to send higher byte of the generated address to the latch. This address is further latched using ADSTB signal.
IOR
It is an active-low bidirectional tri-state input line, which is used by the CPU to read internal registers of 8257 in the Slave mode. In the master mode, it is used to read data from the peripheral devices during a memory write cycle.

## Slide 92
IOW
It is an active low bi-direction tri-state line, which is used to load the contents of the data bus to the 8-bit mode register or upper/lower byte of a 16-bit DMA address register or terminal count register. In the master mode, it is used to load the data to the peripheral devices during DMA memory read cycle.
CLK
It is a clock frequency signal which is required for the internal operation of 8257.
RESET
This signal is used to RESET the DMA controller by disabling all the DMA channels.
Ao - A3
These are the four least significant address lines. In the slave mode, they act as an input, which selects one of the registers to be read or written. In the master mode, they are the four least significant memory address output lines generated by 8257.
CS
It is an active-low chip select line. In the Slave mode, it enables the read/write operations to/from 8257. In the master mode, it disables the read/write operations to/from 8257.

## Slide 93
ADST
This signal is used to convert the higher byte of the memory address generated by the DMA controller into the latches.
AEN
This signal is used to disable the address bus/data bus.
TC
It stands for ‘Terminal Count’, which indicates the present DMA cycle to the present peripheral devices.
MARK
The mark will be activated after each 128 cycles or integral multiples of it from the beginning. It indicates the current DMA cycle is the 128th cycle since the previous MARK output to the selected peripheral device.
Vcc
It is the power signal which is required for the operation of the circuit.

## Slide 94
A4 - A7
These are the higher nibble of the lower byte address generated by DMA in the master mode.
READY
It is an active-high asynchronous input signal, which makes DMA ready by inserting wait states.
HRQ
This signal is used to receive the hold request signal from the output device. In the slave mode, it is connected with a DRQ input line 8257. In Master mode, it is connected with HOLD input of the CPU.
HLDA
It is the hold acknowledgement signal which indicates the DMA controller that the bus has been granted to the requesting peripheral by the CPU when it is set to 1.
MEMR
It is the low memory read signal, which is used to read the data from the addressed memory locations during DMA read cycles.
MEMW
It is the active-low three state signal which is used to write the data to the addressed memory location during DMA write operation.

## Slide 95
ANALOG TO DIGITAL CONVERTER (ADC 0808)
 One technique involves comparing a given analog signal with the internally generated equivalent signal. This group includes Successive approximation Register, counter and flash type converters. It is used
for data loggers and instrumentation
The process of conversion of analog signal to digital signal is referred to as
analog to digital conversion
The system used for realizing this conversion is referred to as an analog-to-digital converter (A/D converter or ADC).
The A/D conversion is a quantizing process where by an analog signal is represented by equivalent binary states. A/D converter can be classified into two groups based on conversion technique.
 The second technique involves changing an analog signal into time or frequency and comparing these new parameters to known values. This group includes Integrator and Voltage to Frequency Converters. It is used in digital meters, panel meters and monitoring system

## Slide 96
Let us see some good features of ADC 0808/0809
The conversion speed is much higher
The accuracy is also high
It has minimal temperature dependence
Excellent long term accuracy and repeatability
Less power consumption
The functional block diagram of this chip is like this
The ADC 0808/0809 Chip
The ADC 0808/0809 is an 8-bit analog to digital converter. It has 8 channel multiplexer to interface with the microprocessor.
This chip is popular and widely used ADC. ADC 0808/0809 is a monolithic CMOS device. This device uses successive approximation technique to convert analog signal to digital form.
One of the main advantage of this chip is that it does not require any external zero and full scale adjustment, only +5V DC supply is sufficient.

## Slide 98
To interface the ADC with 8085, we need 8255 Programmable Peripheral Interface chip with it. Let us see the circuit diagram of connecting 8085, 8255 and the ADC converter.
INTERFACING ADC WITH 8085/8086 MICROPROCESSOR
The PortA of 8255 chip is used as the input port. The PC7 pin of Port Cupper is connected to the End of Conversion (EOC) Pin of the analog to digital converter. This port is also used as input port. The Clower port is used as output port. The PC2-0 lines are connected to three address pins of this chip to select input channels. The PC3 pin is connected to the Start of Conversion (SOC) pin and ALE pin of ADC 0808/0809.
Now let us see a program to generate digital signal from analog data. We are using IN0 as input pin, so the pin selection value will be 00H.

## Slide 99
A Digital to Analog Converter (DAC) converts a digital input signal into an analog output signal. The digital signal is represented with a binary code, which is a combination of bits 0 and 1. This chapter deals with Digital to Analog Converters in detail.
The block diagram of DAC is shown in the following figure